Heat - Solar oven & Smores

Goal: Observe that heat from the sun can be converted into useable energy

Materials:

-Construction box (Pizza box is suggested)

-Two clear sheet protectors

-Black construction paper

-Duct tape

-Clear masking/packing tape

-Box knife (ask teacher for use)

-Scissors

-Thermometer (optional)

-Wooden skewer

-Glue stick

-Tin foil

-Ruler

-Pen

Procedure:

1. On the lid of a pizza box, use a ruler and pen to measure and draw a square that is 1-2" from the sides of the box.

2. Cut along three sides of the square you just made by using box cutters or a pair of scissors.

3. Measure and cut a large piece of foil to line the bottom of the pizza box.

4. Apply glue to the bottom of the pizza box and glue the large piece of foil into place, smoothing in down.

5. Measure and cut another large piece of foil to cover the bottom of the flap you cut on the pizza box lid.

6. Apply glue to the bottom of the pizza box lid and glue the tin foil piece into place.

7. Use scissors to cut a piece of black construction paper that is 1-2" smaller at each edge than the bottom of the pizza box.

8. Use clear masking or packing tape to tape the black construction paper to the bottom of the pizza box. Try to center the black construction paper.

9. Find a sheet protector and pull the two pieces apart. Tape these pieces together at one of their long edges. Tape the new, large piece of plastic on the inside of the box lid, NOT the flap. The plastic should span the flap opening. If it doesn't, make a larger plastic sheet!

10. Use a wooden skewer to poke two small holes (don't poke the skewer all the way through) on the lid between the flap and the side of the lid. Poke the holes about 2" apart.

11. Wrap a thin piece of tape around the skewer, near the flat end, so that one end of the tape is above the other end.

12. Tape the skewer to the flap so that the flat end of the skewer is near the end of the flap. Use the skewer and the holes you poked in the lid as a kickstand for the flap.

13. If you want to see just how hot your Solar Oven gets, tape a thermometer to the bottom of the box so that it can be seen through the plastic window.

14. Set up your oven with the flap up and place it in the sun. It may take a little while, but you'll watch your s'mores heat up, melt, and be ready to eat!

Conclusion:

1. How was your solar oven able to make smores?

2. What could have done to make your solar oven more effective? Explain

http://www.stevespanglerscience.com/lab/experiments/solar-oven